Item 626 Barrier Reflectors

| District: | Date: | Project No.: | Co/Rt/Sec: |
| --- | --- | --- | --- |
| Contractor: | Project/District Contacts: |
| Reviewed “√” | Specification Conformance Statement | CMS/ CIM | Measurements | Conformance Comments |
|  | Barrier Reflectors conform to QPL | 626.02 |  |  |
|  | Barrier Wall Fasteners , brackets adhesives conform to manufacturers recommendations | 626.02 |  |  |
|  | Barrier wall reflector does not extend further than 5 inches toward the traffic lane | 626.02 |  |  |
|  | Layout approved by the engineer | 626.03 |  |  |
|  | Barrier Reflectors placed at the beginning and end of all barrier runs | 626.03 |  |  |
|  | Reflector spacing in the range of 65 to 125 ft on tangents and curves less than 5 degrees | 626.03 |  |  |
|  | Guardrail reflectors placed on blockouts in correct location. | 626.04 |  |  |
|  | All foreign material removed from the surface of the barrier wall and barrier reflector | 626.04 |  |  |
|  | Is the barrier reflector the same color as the edge line | 626.04 |  |  |
|  | Are bidirectional reflectors used on the outside of curves | 626.04 |  |  |
|  | Are pay items documented on the daily diary | 626.05 |  |  |