## Slide 1: 2011 Conaway conference
Value Engineering Change Proposal

## Slide 2: Goals of Value Engineering
Reduce construction costs
offer a time savings in construction without altering the essential functions and characteristics of the project
Encourage the use of the ingenuity and expertise of the Contractor

## Slide 3: ODOT’s New Approach
look to the future by:
Being consistent
Ensuring all VECP’s submitted get due consideration
Timely review, final disposition, implementation, and documentation of VECPs:
  tracks all VECPs
  Monitor, analyze and disseminate the results of all the VECPs implemented.

## Slide 4: Proposed Ways to accomplish this change
  Review of CM&S 105.19:
    Revisit consideration criteria listed
    Update list to allow for more VECP’s
  Revisit Policy and Procedure to allow more opportunities to submit for Time and/or Money
  Revisit the submission process to get all stake holders involved

## Slide 5: ODOT Reviewing w/FHWA
The Department will consider looking into time based VECP’s which will be discussed further with FHWA and the ODOT Committee
Contractors will have the option to request and appeal for all VECP rejections

## Slide 6: Proposed changes to CM&S 105.19
The Department will not approve VECPs with any of the following characteristics:
A. Consist only of non-performing items of work contained in the plans.
B. Include plan errors identified by the Contractor as part of the cost reduction.
C. The VECP designer/consultant for the Contractor is also the designer of record for ODOT.
D. Changes to any special architectural or aesthetic treatments.

## Slide 7: Proposed changes to CM&S 105.19
E. Requires concrete beams to be installed with less than 17' vertical clearance over a state highway.
F. Changes the type or buildup of permanent pavement.
G. Compromises controlling design criteria or would require a design exception as discussed in Volume I, Section 100, of the Location and Design Manual.
H. Have Contractor review the utility note and coordinate with the utility coordinator (District and Central Office) to lessen the impact on the utility.
If the utility has to incur additional costs in order to meet the contractor's VECP request, the contractor must, and is solely responsible for, reimbursing the utility for those costs.

## Slide 8: Characteristics removed from 2010 C&MS 105.19
D. Changes the special architectural aesthetic treatment of structures.
E. Changes the design or thickness of cast-in-place concrete decks.
F. Changes the cross section of geometric design features such as, but not limited to, bridge width, vertical clearance, horizontal clearance, shoulder width.
H. Changes the design of overhead sign supports and breakaway sign supports.
I. Change the type of noise barriers.
J. Changes prescribed sequence of operations for the work as originally contemplated and/or the method for maintaining traffic.
N. Causes additional work, increases the cost, or causes modifications to adjacent projects.

## Slide 9: Proposed Submission Process
All VECP’s must be submitted to the District
District will forward all VECP’s to the Central Office VECP Coordinator (electronic copy is acceptable)
If VECP value is under $50,000, District will accept/deny the proposal and notify the VECP Coordinator
If VECP value is over $50,000, District must include the VECP coordinator in Central Office in the decision.
  The VECP coordinator will send the VECP to the Deputy Director of Construction, Planning and Engineering.
  After review:
    if CO and District agree with the proposed VECP, permission to proceed will be sent to the Contractor.
    If VECP is denied, the Contractor will be given the opportunity to appeal.
A meeting can be requested by either party at any time.

## Slide 10: Annual VECP Accomplishment Report for Federal Fiscal Year 2010
Project Number | CRS | District | Prime Contractor | Description of VE Change | Estimated Savings | Final Disposition | Final CO amount
10-1000 | DEF SR-66 007.37 | 1 | Mosser | Lime stabilization to Geotextile | $ 105,112 | Denied | 
09-8015 | LUC-24 | 2 | Mosser | Lower profile grade | $1,072,987.31 | Approved | $536,494
09-8015 | LUC-24 | 2 | Mosser | Grade separation | $1,323,395.24 | Approved | $661,698
10-1040 | LUC-24 | 2 | E S Wagner | Wheeling St | $77,361.30 | Approved | $38,681
09-0243 | STA-243 | 4 | Beaver Excavating |  | $10,116.00 | Approved | $5,058
09 1058 | POR LR-0 000000 | 4 | Beaver Excavating | 26" Steel case+15" PVC water pipe to 16" DIP on steel frame | $ 73,735 | Approved | $ 36,868
07-0138 | LIC SR-161 006.65 | 5 | Kokosing |  | $ 25,831 | Approved | $12,915.63
09-0513 | FRA-LR-0.00 | 6 | Double Z | Modular block wall in place of plan MSE wall | $ 58,368 | Approved | $29,183.84
09-0513 | FRA-LR-0.00 | 6 | Double Z | Oak handrail and rub rail to galvanized steel w/power coated versus wet paint | $ 26,851 | Approved | $13,425.68
09-0496 | MOT-75-11.01 | 7 | Ruhlin Company | Manhole revision | $ 77,810 | Approved | $38,905
09 0498 | BRO-52-16.16 | 9 | Sunesis Construction | Drilled shaft changes | $ 42,060 | Approved | $21,030
09 1108 | ATH/HOC-33-16.52/0.00 | 10 | Kokosing | Prestressed Pipe to Heavy wall pipe - resubmittal | $ 194,492 | Approved | $97,246
09 1080 | ATH/HOC-33-19.89/1.2 | 10 | Beaver Excavating | Mine Grouting using Deep dynamic compaction | $ 3,122,234 | Denied | 
09 1080 | ATH/HOC-33-19.89/1.2 | 10 | Beaver Excavating | Prestressed Pipe to Heavy wall pipe - resubmittal | $ 75,507 | Approved | $37,754
09 1080 | ATH/HOC-33-19.89/1.2 | 10 | Beaver Excavating | Prestressed pipe to Fusion welded HDPE | $ 298,693 |  | 
09 1108 | ATH/HOC-33-16.52/0.00 | 10 | Kokosing | Profile grade adjustment for earthwork balance | $ 654,764 | Denied | 
09 1108 | ATH/HOC-33-16.52/0.00 | 10 | Kokosing | Revised piling from 33ksi to 50 ksi | $ 286,893 |  | 
09 1108 | ATH/HOC-33-16.52/0.00 | 10 | Kokosing | Mine grouting using deep cut and fill | $ 769,257 |  | $ 384,628.42
09 1080 | ATH/HOC-33-19.89/1.2 | 10 | Kokosing | 42" Special culvert drainage design | $ 75,498 |  | $ 37,749.24
09 1108 | ATH/HOC-33-16.52/0.00 | 10 | Kokosing | Modify Structures HOC-33-1697,1829,1908, and 1986 | $ 403,448 |  | $ 201,724.25
 |  |  |  |  |  | Sum of VECP's | $2,153,359

## Slide 11: VECP program goals and measures Overview
To ensure consistency among the Districts it is recommended that all VECP’s should be sent to Central Office for review before any decision on accepting or denying a VECP is made.
Authorization for rejection of a VECP will be housed at a higher level within the organization than the authorization for approval.
To foster as many innovative proposals as possible specifications are being reviewed to remove restrictions and provide further flexibility as to what VECP’s will be considered.

## Slide 12: Estimating’s Role
Establish GUARANTEED MINIMUM SAVINGS
Notes: Check the costs against the bids.
Establish if new costs are reasonable.
To assist in assuring the Standard Procedure for Value Engineering In Construction Policy is followed as it pertains to costs and savings.

## Slide 13: Standard Procedure
  Standard Procedure for Value Engineering In Construction, Policy No. 510-008(SP), effective 2/1/2010
    The SOP states: The purpose of this provision is to encourage the use of ingenuity and expertise of the Contractor …….....
Notes: Underlined use of ingenuity and expertise of the Contractor to emphasize that the VECP’s are not simply pay for items that are being non-performed or taking what Departmental changes have been asked for.

## Slide 14: Preliminary Submittal
The Contractor will submit the following as part of a VECP:
  Separate detailed cost estimates for both the existing contract requirements and the proposed change. The cost estimates shall be broken down by contract item numbers indicating quantity increases or decreases and deleted pay items.
  Additional proposed work, not covered by contract items, shall be identified by current Department pay item numbers. In preparing the estimates, the contractor shall include overhead and profit. No separate pay items are allowed for these costs.
Notes: To Summarize - VECP shall include:
Item number – original contract qty - original contract bid price – new qty
All new items of work shall include a Department Pay Item Number and description.

## Slide 15: Items of Concern
PARTIAL Lump sum items
VECP’s that state “will secure actual quantities as design or construction occur”.
Items that appear to be removed as non-performed but put back in as ‘New Work’ with different cost.
VECP items that in original bid appear to have been bid with VECP in mind.
Notes: Lump Sum – hard to estimate has changed, what's already been done and a fair price.
Changing Qty’s – we set a GUARANTEED MINIMUM SAVINGS. Accepting these sets us up to lose that!
If the same or similar work as original bid is being performed it must be performed at the original bid price.
The Bidding Process can be harmed at a date later than the bid opening… meaning we have found VECP’s that were bid and they affect items that obviously have been manipulated in the bidding process with the VECP in mind.

## Slide 16
VECP sample # 1
Notes: This is a template in Excel of proper way to summarize and submit costs for VECP. We can provide this template to anyone that would like a copy.

## Slide 17
VECP sample # 2
Notes: Good use of format. Easy to follow.
Large qty changes for an entire operation will get some extra scrutiny but looks good on surface.

## Slide 18: VECP sample # 3
Notes: No references.
No original bids.
No item numbers.
No qty changes.
No Plans.
Lump sum total??? How do we estimate this? SEE NEXT SLIDE.

## Slide 19
Notes: Obviously time can be saved if we submit properly the first time.

## Slide 20: ODOT Project 467(06) SR 8/I-271 Reconstruction City of Macedonia VECP Proposal

## Slide 21
July 2006

## Slide 22
October 2009
Old ramp eliminated
New on-ramp

## Slide 23: Typical Geologic Cross-Section
Multiple glacial advances/retreats filled valley with soft/loose and compressible glaciofluvial and glaciolacustrine sediments (A-4 to A-6 soils); Flat, poorly draining topography, and adjacent streams left soft, organic deposits near the ground surface; High static groundwater table – within 10 ft of ground surface over project.

## Slide 24: Engineering Properties of Soils
Key Observations: Glaciolacustrine soils are soft/loose materials based on SPT results and visual descriptions, but all are overconsolidated. Piezocone testing indicates that non-plastic silts (A-4a and A-4b) dissipate pore pressures 2-3 orders of magnitude faster than soils with higher plasticity and clay content.

## Slide 28
Typical Undercut Backfill Section
Undercut Depth
Type D Geotextile
Type D Granular
Original Grade
Embankment
3-5 ft

## Slide 29
Typical Undercut Backfill Configuration
Type D Geotextile
Type D Granular
Original Grade
Embankment
3-5 ft
Undercut Depth
– with Wick Drains
18” Type E Granular
Wick drain (TYP)

## Slide 30: Final VECP Proposal SUM 467(06)
Modifies the embankment subgrade improvement plan and pavement subgrade improvement plan
Replace the total thickness of granular with reduced thickness and layers of fabrics and grids.
Raises elevation of drainage layer to allow more positive drainage
7 embankment scenarios
2 pavement scenarios

## Slide 31: VECP Proposal
Fabric on bottom of undercuts prevents contamination of drainage layer
Grid supplier Contech- fabric does not reduce structural properties of the grid
Wick drains outlet in higher drainage level
Improvement below MSE walls changed to sand to prevent piping into stabilized materials

## Slide 32
Item | Description | Unit | Quantity | Total
203 | Embankment | CY | 28,092 | $ (268,278.60)
204 | Excavation of Subgrade | CY | 100,689 | $ (662,533.62)
204 | Granular Material, Type D, APP | CY | 112,285 | $(2,739,754.00)
204 | Granular Material, Type E, APP | CY | 22,648 | $ (612,175.44)
Non-Performed Items
$ (4,282.741.66)
203 | Wick Drains w/o Predrilling | FT | 19,069 | $ 9,343.81
204 | Granular Material, Type B | CY | 18,112 | $ 312,432.00
204 | Geotextile Fabric | SY | 102,596 | $ 112,855.50
304 | Aggregate Base | CY | 685 | $ 26,030.00
204 | Granular Material, Type C | CY | 9,105 | $ 309,205.80
204 | Granular Material, Type F | CY | 34,465 | $ 899,191.85
Sp | Geogrid Tensar BX-1200 | SY | 266,911 | $ 1,267,827.25
Sp | Geogrid Tensar BX-1300 | SY | 27,314 | $ 119,635.32
Additional Items
$ 3,056,521.63

## Slide 33
Non-Preformed $ 4,282,741.66
Additional Items $ 3,056,521.63
Total Savings $ 1,226,220.03
50/50 Split $ 613,110.02
Cost Savings

## Slide 34
Detail “A”
Original Grade
VECP Proposal

## Slide 35
Detail “A”
12” Undercut
Original Grade
VECP Proposal

## Slide 36
Detail “A”
12” Undercut
8oz Geotextile
Original Grade
VECP Proposal

## Slide 37
Detail “A”
12” Undercut
8oz Geotextile
BX-1200 Geogrid
Original Grade
VECP Proposal

## Slide 38
Detail “A”
12” Undercut
8oz Geotextile
BX-1200 Geogrid
12” Granular Type E
Original Grade
VECP Proposal

## Slide 39
Detail “A”
12” Undercut
8oz Geotextile
BX-1200 Geogrid
12” Granular Type E
BX-1200 Geogrid
Original Grade
VECP Proposal

## Slide 40
Detail “A”
12” Undercut
8oz Geotextile
BX-1200 Geogrid
12” Granular Type E
BX-1200 Geogrid
12” Granular Type D
Original Grade

## Slide 41
Detail “A”
12” Undercut
8oz Geotextile
BX-1200 Geogrid
12” Granular Type E
BX-1200 Geogrid
12” Granular Type D
Type D Geotextile
Original Grade

## Slide 42
Detail “A”
12” Undercut
8oz Geotextile
BX-1200 Geogrid
12” Granular Type E
Wick drain (TYP)
BX-1200 Geogrid
12” Granular Type D
Type D Geotextile
Original Grade

## Slide 43
Detail “A”
12” Undercut
8oz Geotextile
BX-1200 Geogrid
12” Granular Type E
Wick drain (TYP)
Embankment
BX-1200 Geogrid
12” Granular Type D
Type D Geotextile
Original Grade

## Slide 44
Detail “B”
Original Grade
VECP Proposal

## Slide 45
Detail “B”
26” Undercut
Original Grade
VECP Proposal

## Slide 46
Detail “B”
26” Undercut
8oz Geotextile
Original Grade
VECP Proposal

## Slide 47
Detail “B”
26” Undercut
8oz Geotextile
BX-1200 Geogrid
Original Grade
VECP Proposal

## Slide 48
Detail “B”
26” Undercut
8oz Geotextile
BX-1200 Geogrid
13” Fine Aggregate
Original Grade
VECP Proposal

## Slide 49
Detail “B”
26” Undercut
8oz Geotextile
BX-1200 Geogrid
13” Fine Aggregate
BX-1200 Geogrid
Original Grade

## Slide 50
Detail “B”
26” Undercut
8oz Geotextile
BX-1200 Geogrid
13” Fine Aggregate
BX-1200 Geogrid
13” Fine Aggregate
Original Grade

## Slide 51
Detail “B”
26” Undercut
8oz Geotextile
BX-1200 Geogrid
13” Fine Aggregate
BX-1200 Geogrid
Type D Geotextile
13” Fine Aggregate
Original Grade

## Slide 52
Detail “B”
26” Undercut
8oz Geotextile
BX-1200 Geogrid
13” Fine Aggregate
BX-1200 Geogrid
Wick drain (TYP)
Type D Geotextile
13” Fine Aggregate
Original Grade

## Slide 53
Detail “B”
26” Undercut
8oz Geotextile
BX-1200 Geogrid
13” Fine Aggregate
BX-1200 Geogrid
Wick drain (TYP)
MSE wall
Select
Granular
Embankment
13” Fine Aggregate
Original Grade
Type D Geotextile

## Slide 54
Detail “C”
26” Undercut
8oz Geotextile
BX-1200 Geogrid
13” Type E Granular
BX-1200 Geogrid
Wick drain (TYP)
Type D Geotextile
13” Type E Granular
Embankment
12” Type D Granular
Original Grade

## Slide 55
Detail “D”
24” Undercut
8oz Geotextile
BX-1200 Geogrid
12” Fine Aggregate
BX-1200 Geogrid
12” Fine Aggregate
Wick drain (TYP)
Type D Geotextile
MSE wall
Select
Granular
Embankment
Original Grade

## Slide 56
Detail “E”
12” Undercut
8oz Geotextile
BX-1200 Geogrid
12” Granular Type E
Wick drain (TYP)
BX-1200 Geogrid
12” Granular Type D
Type D Geotextile
Embankment
Original Grade

## Slide 57
Detail “P-1”
36” Undercut
Type D Geotextile
24” Type D Granular
Type D Geotextile
12” Type B Granular
Proposed Pavement
Original Grade
VECP Proposal

## Slide 58
Geogrid for Subgrade Stabilization
Supplemental Specification 861
October 15, 2010
Work consisting of furnishing and installing biaxial geogrid for the purpose of stabilizing subgrade.
Place geotextile fabric on bottom if specified

## Slide 91: June 2007Looking NB 8 /Ramp A,B to left

## Slide 92: January 2008 I271 bottom/ Ramp A-B at the top

## Slide 95
4/15/08

## Slide 96: July 2006 October 2009

## Slide 97
Questions