## Slide 2
2016 Construction & Materials Specifications
Performance Specification 611

## Slide 3: Item 611 Specification
Fall of 2015 SS800 & 2016 Book
  611.04 Installation Plans require CA-P-1A and CA-P-3A – Becomes part of the Contract
  Cross-sections & manufacturer sign off still required

## Slide 4: Item 611 Specification
Fall of 2015 SS800 & 2016 Book
  611.04 Construction Inspections require CA-P-1 and CA-P-3
Verification of as-built elevations
Formerly part of performance survey
Out of tolerance construction requires evaluation – Contractor’s risk

## Slide 5: Item 611 Specification
Fall of 2015 SS800 & 2016 Book
  CA-P-3 not required for precast concrete outlet structures

## Slide 6: Item 611 Specification
Fall of 2015 SS800 & 2016 Book
  611.13 Conduit Evaluation
    Engineer must document all defects and provide evaluation.
      Table 611.13 and LRFD Bridge Construction Specification Sections 26, 27 & 30
      Metal conduits – racking is to be measured on structural plate conduits
      Concrete conduits – cracks are to be evaluated at 0.01-in
      Thermoplastic conduits – flattening or racking at installation

## Slide 7: Item 611 Specification
Fall of 2015 SS800 & 2016 Book
  611.13 Conduit Evaluation
    Evaluate defects for structural stability & hydraulic capacity
    Hydraulic analysis intended for out of tolerance installations
    Repairs require follow-up inspection and evaluation - 30-90 day waiting period applies

## Slide 8: Item 611 Specification
Fall of 2015 SS800 & 2016 Book
  Table 611.13
    Evaluate vertical alignments from CA-P-1
    Sags require hydraulic and structural evaluation
    Joint gaps 100% within manufacturer’s tolerance
    Cap repairs of flexible conduits at 12%
      Deflections exceeding 7.5% require further measurements

## Slide 9: Item 611 Specification
Fall of 2015 SS800 & 2016 Book
  611.14 Drainage Structure Evaluation
    Added similar language to 611.13
  Table 611.14
    Inspect construction and connections, not just infiltration
    Invert elevation of connected conduits ref. CA-P-1
    Grate elevation ref. CA-P-3

## Slide 10: Item 611 Specification
Inspections and Evaluations

## Slide 11: Item 611 Specification
Inspections and Evaluations

## Slide 12: Item 611 Specification
Inspections and Evaluations

## Slide 13: Item 611 Specification
Inspections and Evaluations

## Slide 14: Item 611 Specification
Inspections and Evaluations

## Slide 15: Item 611 Specification
Inspections and Evaluations

## Slide 16: Item 611 Specification
Rerounding Repairs

## Slide 17: Item 611 Specification
Rerounding Repairs

## Slide 18: Panel Discussion
Ted Wellman, The Beaver Excavating Company
Greg Hamilton, Kokosing Construction Company
Mike Murphy, ODOT District 1 Area Engineer
Hans Gucker, ODOT Central Office Construction Administration