## Slide 1: Determining Seismic Hazard
General
Earthquakes and Ground Motion in Ohio
Site Classification
Site Factors
Seismic Performance Zones
Worked Examples
Geotechnical Engineer’s Input

## Slide 2: What’s this all about?
AASHTO 3.10.1
“Bridges shall be designed to have a low probability of collapse,. . . . . . . . . . . when subject to earthquake ground motions that have a 7% probability of exceedance in 75 yrs” (about 1 in 1000 yr return period).

## Slide 3: How do we do that?
We need to understand how seismically induced ground motion and structure components interact.
Washington Cathedral
Virginia Event 2011

## Slide 4
Structure of
Interest
Energy Propagation
In Soil
Energy Propagation
In Rock as ground motion
Epicenter Distance
Earthquake
Magnitude
M
Fault Rupture
(Epicenter)

## Slide 5
There are several parts to the puzzle:
A causative event (earthquake) to create ground motion.
A structure to shake (bridge).
A physical connection between the two (earth).
A body of science upon which to base engineering practice (seismology, earthquake engineering)
Codification of appropriate engineering practice (AASHTO LRFD, ODOT BDM etc)
Notes: In this session we'll be dealing with 1 and 3, a little of 4 and quite a lot of 5

## Slide 6: Seismic Hazard
How do we define or describe a seismic hazard?
Earthquake magnitude?
Earthquakes are always classified on a logarithimic scale, usually 1 – 10, so that 7.0 is 100 times stronger than 5.0 and 8.0 is 1000 times stronger than 5.0

## Slide 7
Distance to Epicenter
(500 miles is better for your structure than 5 miles)

## Slide 8: Site Conditions
Can have a significant local effect by amplifying ground motion.
Frequency of Occurrence
-Infrequent is best!

## Slide 9: To understand the physical connections, we start by relating earthquake magnitude to ground motion.

## Slide 10
Earth scientists study this – at places like:
Pacific Earthquake Engineering Research Center UC Berkeley
Multidisciplinary Center for Earthquake Engineering Research The University at Buffalo
Mid-America Earthquake Center University of Illinois At Urbana-Champaign
USGS – Research and monitoring world-wide.

## Slide 11
Intermediaries synthesize research findings into usable engineering principles as published in such documents as:
LRFD Bridge Design Specifications AASHTO (2014, and interims)
Recommended LRFD guidelines for the Seismic Design of Highway Bridges (Applied Technology Council and Multidisciplinary Center for Earthquake Engineering Research (ACT/MEER)
ODOT Bridge Design Manual

## Slide 12
USGS, together with the various research organizations, developed models that are used to predict what is called the MCE –
Maximum Considered Earthquake
A “maximum considered earthquake” (MCE) for a specific area, is an earthquake that is expected to occur once in approximately 2500 yrs; that is, it has a 2% probability of being exceeded in 50 yrs.
Notes: Ok – back to the process we have to follow

## Slide 13: Code Reference Documents Considered by USGS:
2012 International Building Code
2010 ASCE/SEI 7 Standard
2003 NEHRP Recommended Provisions
2009 AASHTO Guide Specifications for LRFD Seismic Bridge Design (7% in 75 yrs probability of occurrence)

## Slide 14
Ohio is on the fringe of the New Madrid Seismic Zone. We get the left-overs from any event that occurs on that system.
Leftovers can be a problem - Cincinnati experienced some damage in the 1811/12 event.
Earthquakes and Ground Motion in Ohio
Notes: This is a nice seque back to Ohio seismology.

## Slide 15
‘Home Grown’ Ohio Earthquakes
New Madrid Seismic Zone

## Slide 16
Ohio has experienced ~230 small earthquakes (>2.0) and a few medium events (<5.4) since mid-18th century.

## Slide 18
‘Anna’
Area

## Slide 19
Note a correlation with the 1880-1940 period of peak
hydrocarbon (gas and crude oil) extraction in this area.
Northwest Ohio
1888

## Slide 20
Lake and Ashtabula
counties – Note the correlation
with operations
of a deep well
injection system from mid-1980’s to early 2000’s
in this area.

## Slide 21
Here’s the Youngstown Area – Note correlation with recent fracking and deep well disposal operations post 2000.

## Slide 22
Which is more critical -
A magnitude 7.7 earthquake on the New Madrid Fault 500 miles away or a magnitude 5.4 earthquake on an unknown fault in northeast Ohio 3 miles from your new bridge?

## Slide 23
To get a general idea, we can use a Ground Motion Prediction Equation (GMPE)
Cornell's Method (1979)
ln Ap = 6.74 + 0.859 * Ml – 1.8 * ln (R + 25)
Ap = Peak Ground Acceleration (cm/s2)
Ml = Magnitude R = distance (km)
Note: 289 GMPE equations published 1964-2010 for PGA.
Notes: remember that this has largely been replaced by more complex PSHA tools (probabilistic seismic hazard analysis) - but may have some merit for local studies that the national programs can't cover
Equation, explain input variables

## Slide 24
Notes: remember that this has largely been replaced by more complex PSHA tools (probabilistic seismic hazard analysis) - but may have some merit for local studies that the national programs can't cover
Equation, explain input variables

## Slide 25: Spectral Acceleration – What is it?
Raw
Accelerograph
Record
Convert this to something that can be useful for design
Develop a Design Response Spectrum
Displays Maximum Acceleration for a range of ground motion periods

## Slide 26: Construction of the Raw Design Spectrum
Input:
PGA – Peak Ground Acceleration
Ss – short period Spectral Acceleration
S1 – long-period Spectral Acceleration
Apply Site Specific Factors
PGA
Ss
S1

## Slide 27: Site Classification – Why is it important?
To Develop Site Specific Factors required to construct the Design Spectrum.

## Slide 28: Site Class Definitions
Site Class | Soil Profile Name | Average Properties in Top 100 ft |  | 
 |  | Soil Shear Wave Velocity | Standard Penetration Resistance | Soil Undrained Shear Strength
A |  |  |  | 
B |  |  |  | 
C |  |  |  | 
D |  |  |  | 
E |  |  |  | 
E may, together with F, be a special case – very weak soils.

## Slide 29: Site Class Definitions (consider upper 100 ft)
Site Class | Soil Profile Name | Soil Shear Wave Velocity, v s, (ft/s)
A | Hard rock | vs > 5,000
B | Rock | 2,500 < vs < 5,000
C | Very dense soil and soft rock | 1,200 < vs < 2,500
D | Stiff Soil Profile | 600 < vs < 1,200
E | Soft Soil Profile | vs < 600
Difficult to measure – Can use seismic CPT or published values,
with caution; only basis to classify sites as A or B.

## Slide 30
Shear Wave Velocity Estimates
Soil/Rock Type | P Wave ft/s | S Wave ft/s | Site Class
Scree, vegetal soil | 1000-2300 | 330-1000 | D/E
Dry sands | 1300-3900 | 330-1640 | C/D/E
Wet sands | 4900-6600 | 1300-2000 | C
Saturated shales and clays | 3600-8200 | 660-2600 | B/C/D
Marls | 6600-9800 | 2500-5000 | B
Saturated shale and sand sections | 4900-7200 | 1640-2500 | B/C
Porous and saturated sandstones | 6600-11500 | 2600-5900 | A/B
Limestones | 11500-19600 | 6600-10800 | A
Dolomite | 11500-21300 | 6200-11800 | A
Coal | 7200-8900 | 3300-4600 | B
Classification Criteria |  | 
and below | 600 | E
600 | 1200 | D
1200 | 2500 | C
2500 | 5000 | B
5000 | and above | A

## Slide 31: Site Class Definitions
Site Class | Soil Profile Name | Standard Penetration Resistance, N
A | Hard rock | NA
B | Rock | NA
C | Very dense soil and soft rock | N > 50
D | Stiff Soil Profile | 15 < N < 50
E | Soft Soil Profile | N < 15

## Slide 32: Site Class Definitions
Site Class | Soil Profile Name | Soil Undrained Shear Strength, su , (ksf)
A | Hard rock | NA
B | Rock | NA
C | Very dense soil and soft rock | su > 2.0
D | Stiff Soil Profile | 1.0 < su < 2.0
E | Soft Soil Profile | su < 1.0

## Slide 33: Site Class Definitions
Site Class | Soil Profile Name | Soil Shear Wave Velocity | Standard Penetration Resistance | Soil Undrained Shear Strength
E | - | Any profile with more than 10 ft of soil having the following characteristics: Plasticity index PI > 20, Moisture Content w > 40%, and Undrained shear strength su < 500 psf |  | 

## Slide 34: Site Class Definitions
Site Class | Soil Profile Name | Soil Shear Wave Velocity | Standard Penetration Resistance | Soil Undrained Shear Strength
F | - | Any profile containing soils having one or more of the following characteristics: Soils vulnerable to potential failure or collapse under seismic loading such as liquefiable soils, quick and highly sensitive clays, collapsible weakly cemented soils. Peats and/or highly organic clays (H > 10 ft of peat and/or highly organic clay where H = thickness of soil) Very high plasticity clays (H > 25 ft with plasticity index PI > 75 Very thick soft/medium stiff clays (H > 120 ft) |  | 

## Slide 35
Soil Cover
Thickness

## Slide 36
Site Class | PGA1 | <0.10 | 0.20 | 0.30 | 0.40 | >0.50
 | Ss1 | <0.25 | 0.50 | 0.75 | 1.00 | >1.25
A |  | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
B |  | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
C |  | 1.2 | 1.2 | 1.1 | 1.0 | 1.0
D |  | 1.6 | 1.4 | 1.2 | 1.1 | 1.0
E |  | 2.5 | 1.7 | 1.2 | 0.9 | 0.9
F 2 |  |  |  |  |  | 
1 | Use straight-line interpolation for intermediate values. |  |  |  |  | 
2 | Site-specific geotechnical investigation and dynamic site response analysis should be performed for all sites in Site Class F. |  |  |  |  | 
Values of Site Factors Fpga and Fa (AASHTO)
Tables 3.10.3.1-1 and -2.
<0.10
<0.25
0.8
1.0
1.2
1.6
2.5

## Slide 37
Site Class | Spectral Acceleration Coefficient At Period 1.0 sec (S1)1 |  |  |  | 
 | <0.1 | 0.2 | 0.3 | 0.4 | 0.5
A | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
B | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
C | 1.7 | 1.6 | 1.5 | 1.4 | 1.3
D | 2.4 | 2.0 | 1.8 | 1.6 | 1.5
E | 3.5 | 3.2 | 2.8 | 2.4 | 2.4
F 2 |  |  |  |  | 
1 | Use straight-line interpolation for intermediate values. |  |  |  | 
2 | Site-specific geotechnical investigation and dynamic site response analysis should be performed for all sites in Site Class F. |  |  |  | 
Values of Site Factors Fv (AASHTO)
<0.1
0.8
1.0
1.7
2.4
3.5

## Slide 38
For the purpose of determining the Seismic Hazard Level for Site Class E Soils (Article 3.4.2.3) the value of Fv and Fa need not be taken larger than 2.4 and 1.6, respectively, when S1 is less than or equal to 0.10 and Ss is less than 0.25.

## Slide 39
(2) For the purposes of determining the Seismic Hazard Level for Site Class F Soils (Article 3.4.2.3) Fv and Fa values for Site Class E soils may be used with the adjustment described in Note 1 above.

## Slide 40
Site Class | Ss1 | <0.25 | 0.50 | 0.75 | 1.00 | >1.25
A |  | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
B |  | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
C |  | 1.2 | 1.2 | 1.1 | 1.0 | 1.0
D |  | 1.6 | 1.4 | 1.2 | 1.1 | 1.0
E |  | 1.6 | 1.7 | 1.2 | 0.9 | 0.9
F |  | 1.6 |  |  |  | 
1 | Use straight-line interpolation for intermediate values. |  |  |  |  | 
Values of Site Factor Fa (ODOT)
ODOT BDM – use site factors for Site Class D for Site Class E and F (S.3.10.3.2).
Site Class | Ss1 | <0.25
A |  | 0.8
B |  | 1.0
C |  | 1.2
D |  | 1.6
E |  | 1.6
F |  | 1.6
Fpga remains unchanged from AASHTO.

## Slide 41
Site Class | Spectral Acceleration Coefficient At Period 1.0 sec (S1)1 |  |  |  | 
 | <0.1 | 0.2 | 0.3 | 0.4 | 0.5
A | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
B | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
C | 1.7 | 1.6 | 1.5 | 1.4 | 1.3
D | 2.4 | 2.0 | 1.8 | 1.6 | 1.5
E | 2.4 | 3.2 | 2.8 | 2.4 | 2.4
F | 2.4 |  |  |  | 
1 | Use straight-line interpolation for intermediate values. |  |  |  | 
Values of Site Factors Fv (ODOT)
ODOT BDM – use site factors for Site Class D for Site Class E and F (S.3.10.3.2).
Site Class | Spectral Acceleration Coefficient At Period 1.0 sec (S1)1 |  |  |  | 
 | <0.1 | 0.2 | 0.3 | 0.4 | 0.5
A | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
B | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
C | 1.7 | 1.6 | 1.5 | 1.4 | 1.3
D | 2.4 | 2.0 | 1.8 | 1.6 | 1.5
E | 2.4 | 3.2 | 2.8 | 2.4 | 2.4
F | 2.4 |  |  |  | 
1 | Use straight-line interpolation for intermediate values. |  |  |  | 

## Slide 42: How does it work?
Ground Motion (PGA, Ss, S1)
+
Site Classification (A-F)
+
Site Factors (Fpga, Fs, Fv)
Design Response Spectrum
(Design Acceleration = Acceleration * Site Factor)
Seismic Zone Determination (1-4)

## Slide 43
Table 3.10.6.1 – Seismic Zones
ODOT BDM S.3.10.3.2) ‘All bridges in Ohio are located within Seismic Performance Zone 1’.
Acceleration Coefficient SD1 | Seismic Zone
SD1 < 0.15 | 1
0.15 < SD1 < 0.30 | 2
0.30 < SD1 < 0.50 | 3
0.50 < SD1 | 4
SD1 < 0.15 | 1
SD1 is the 1-second period spectral design acceleration – S1 * Fv

## Slide 44: Construction of Design Response Spectrum
Using LRFD
Figures 3.10.2.1-1 through 21
PGA = 0.3s
Ss = 0.5s
S1 = 0.2s
Site Class = C

## Slide 46
BDM Fig 301.4.1.1-1
SD1 = S1 * FV
if SD1 > 0.15 and Fv = 3.5
S1 > 0.15/3.5 = 0.042
(4.2%g)

## Slide 47
Determine Site Class ‘designer shall analyze soil borings………..’ LRFD 3.10.3.1
Is Site Class
A, B or C?
All bridges in Ohio are in Seismic Performance Zone 1 SD1 <= 0.15
Is Site Class F?
Is S1 >=0.042?
(Fig 301.4.4.1-1)
Is 0.1<SD1<0.15?
(use Fv=2.4)
Consider only
BDM 304.4.4.1a
BDM 304.4.1b
Consider BDM
301.4.4.1a, 301.4.4.1b
LRFD 5.10.11.4.1d,
5.10.11.4.1e
YES
YES
NO
NO
YES OR UNKNOWN
NO
NO
YES
BDM
301.4.4.2a

## Slide 51
Lucas Bridge 75-0167
Depth | su | 
 | B-093 | B-040
0 | 3 | 3.75
 | 3.5 | 4.5
 | 3.2 | 4.5
 |  | 3
 |  | 2.5
10 | 4 | 1
 | 3.9 | 0.25
 | 3.4 | 0.25
 | 3.8 | 0.25
20 | 1.3 | 0.25
 | 0.75 | 0.25
 | 0.75 | 0.75
 | 0.62 | 
30 | 0.75 | 1.1
 | 0.87 | 1
40 | 1.2 | 1.3
 | 1.7 | 2
50 | 1.7 | 2.6
 | 2.3 | 2.2
60 | 2.6 | 2.8
 | 2.3 | 1.25
70 | 0.5 | 1.1
 | 0.5 | 0.25
80 | 0.82 | 4.5
 | 4.5 | 4.5
90 | 4.5 | 4.5
 | 4.5 | 4.5
100 | 4.5 | 

## Slide 52
Lucas Bridge 75-0167
Summary by Layer |  |  |  |  | 
i | sui | from | to | di | di/sui
1 | 3.6 | 0 | 15 | 15 | 4.17
2 | 0.62 | 15 | 40 | 25 | 40.32
3 | 1.43 | 40 | 50 | 10 | 6.99
4 | 2.47 | 50 | 65 | 15 | 6.07
5 | 0.74 | 65 | 80 | 15 | 20.27
6 | 4.5 | 80 | 100 | 20 | 4.44
7 | - | - | - | - | -
 |  |  |  | Σ di/su i | 82.27
 |  | Σ di | 100 | Class | 
 |  | Σ di/Σdi/sui Ave su i | 1.22 | D | 
Note: For Cohesive soils, Su is more reliable than N.

## Slide 53
Depth | N60 | 
 | B-093 | B-040
0 | 11 | 18
 | 14 | 16
 | 16 | 15
 |  | 20
 |  | 5
10 | 14 | 5
 | 14 | 1
 | 16 | 3
 | 12 | 1
20 | 12 | 5
 | 8 | 4
 | 8 | 7
 | 9 | 8
30 | 8 | 9
 | 8 | 9
40 | 12 | 14
 | 12 | -
50 | 26 | 26
 | 20 | 24
60 | 24 | 30
 | 16 | 22
70 | 12 | 16
 | 3 | 1
80 | 12 | 34
 | 53 | 68
90 | 61 | 85
 | 53 | 80
100 | 100 | 72
Lucas Bridge 75-0167
EXAMPLE 1
Site Classification

## Slide 54
Lucas Bridge 75-0167
Summary by Layer |  |  |  |  | 
i | Ni | from | to | di | di/Ni
1 | 15 | 0 | 15 | 15 | 1.00
2 | 6 | 15 | 40 | 25 | 4.17
3 | 13 | 40 | 50 | 10 | 0.77
4 | 22 | 50 | 75 | 25 | 1.14
5 | 2 | 75 | 80 | 5 | 2.50
6 | 62 | 80 | 100 | 20 | 0.32
7 | - | - | - | - | -
 |  |  |  | Σ di/Ni | 9.89
 |  | Σ di | 100 | Class | 
 |  | Σ di/Σdi/Ni Ave Ni | 10 | E | 
Note: Ni should be based on the N60 not raw N values (BDM S.10.3.1).

## Slide 55
Lucas Bridge 75-0167
Design Response Spectrum

## Slide 56
Fairfield County, Ohio

## Slide 57
Fairfield County, Ohio
Forward Abutment – Rock (Sandstone)
2600 < Vs < 5900 ft/s – B
Rear Abutment – 50 ft embankment + overburden
50 ft rock (sandstone)
i | Vsi | from | to | di | Di/Vsi
1 | 500 | 0 | 50 | 50 | 0.1
2 | 2500 | 50 | 100 | 50 | 0.02
 |  |  |  | Σdi/Vsi | 0.12
 |  | Σdi | 100 | Class | 
 |  | Σdi/Σdi/Vsi |  |  | 
 |  | Ave Vs | 833 ft/s | D | 

## Slide 62
HAM-Western Hills Viaduct
Mill Creek Crossing
Abutment – Rock (Shale)
Vs = 1700 ft/s
Soil Class C
Piers – soft clay – Soil Class E (AASHTO)
Soil Class D (ODOT)
Soil Class | SD1 | 
C | 0.080 | (<0.1)
D | 0.113 | (>0.1) (SPZ 1-BDM)
E | 0.165 | (SPZ 2 – AASHTO)

## Slide 63: What information should be provided by the Geotechnical Engineer?
In an ideal world……..
The Geotechnical Designer is responsible for providing geotechnical/seismic parameters to the Structural Engineers for their use in structural design. Specific elements include:
Design ground motion parameters
Site Response
Input for evaluation of soil-structure interaction (foundation response to seismic loading), earthquake induced earth pressures on retaining walls
Assessment of the impacts of geologic hazards on the structures