## Slide 1: Item 611 Update
Performance Based Specification
Hans Gucker, P.E.

## Slide 2: 611 Spec Update
Recent Spec Changes – January 2015
  Require geotextile fabric over coarse aggregate backfill
  Final Backfill shall meet requirements of Item 203

## Slide 3: 611 Review
Contractor selects conduit material
Works with conduit manufacturer to develop installation plan
Installs pipe & provides installation documentation
Provides performance evaluation
Inspections
Testing
Findings reviewed by 3rd party engineer

## Slide 4: 611 Project Submittals
Shop Drawings (as required)
Installation Plan
Construction Inspection Forms
Performance Report
Critical elements of the performance spec

## Slide 5: Shop Drawings
Two cases where shop drawings get forwarded on
  Load rating calculations (structures under ODOT road)
    Send to District P&E Eng. forward to OSE
  Change in structure type – verify hydraulic design
    Send to District Hyd. Eng. forward to OHE
Signed by registered engineer (language revised in 800 – One Engineer only)
Department has 15 days for the review

## Slide 6: Installation Plans
Needs to be specific… general
  8 items required – for each run
  Manufacturer must sign off on installation plan
  Revised installation method or material requires a revised plan (signed by manufacturer)

## Slide 7: Installation Plans
Field Observations
  Small culvert projects still problematic
  Incomplete – not all runs or structures
  Slow & Unorganized
  Backfill material or compaction changing during construction
  Manufacturers not reviewing plan

## Slide 8: Installations Plans
Backfill material
  All backfill & bedding material required to be identified – with compaction
  Structural and Final backfill now defined
Bedding
Structural Backfill
Final Backfill
Conduit/Culvert
Final Backfill
CMS Item 203
Manufacturers only review for structural component of conduit

## Slide 9: Installations
Coarse aggregate backfill
  Still requires geotextile below groundwater
  Geotextile fabric over course aggregate
Bedding
Course Aggregate #57’s
Fine Graded
Conduit/Culvert
Geotextile fabric
Geotextile fabric

## Slide 10: Construction Inspections
Performed by Contractor
Documents compliance with installation plan – Quality Control
Modified installation - require modified installation plan
Density testing included

## Slide 11: Construction Inspections
Field Observations
  Poor quality or minimal inspections – untrained personnel
  Rubber stamped inspection forms
  Transfer of inspection forms has been typically slow or not occurring
  Modifying installation - without informing Engineer

## Slide 12: Performance Reports
Final submittal – documents performance
  Includes Performance Inspection
  Independent Engineer evaluation
  Location data Types A & B
District should not accept work if all information is not present
  Evaluation needs to identify all deficiencies
Performance Inspection
Evaluation
Performance Report
Recommendations

## Slide 13: Performance Inspection
Only (Type A, B & C) conduits and structures
Performed 30-90 day after installation period – based on each conduit phase
  Begins after rough subgrade compaction
Manual or remote – both require video
Independent Engineer evaluates findings
30 day waiting period may be waived
  Very few instances when waiver applies
    No access to conduit
    Inspection needs to be planned into work

## Slide 14: Performance Inspection
Field Observations
  Only parts of a conduit inspected
    All joints…not only some
  Manual inspection not videoed
  Surface settlements not observed
  Mandrels not meeting size requirements
    Based on nominal pipe size reference SS902

## Slide 15: Inspection Videos
Field Observations
  Remote inspections require crawler mounted camera per SS902
  Ability to measure cracks and joint gaps
  Consider how files are presented to project
    Organize so run can be identified by file name
    File size
    Ensure material can be retrieved
      CD’s with paper cover can become unreadable
  Project Examples…
    O:\Construction\Gucker\D1 Construction School\31-D6-D7.mpg
    O:\Construction\Gucker\D1 Construction School\vertical sag 130558_CB 3A-CB 3A_10282014.wmv

## Slide 16: Engineer Evaluations
No noted deficiency in evaluation

## Slide 17: Engineer Evaluations
Vertical sag not noted in evaluation

## Slide 18: Engineer Evaluations
Horizontal deflection at beginning of pipe – not noted

## Slide 19
Racking vs. Deflection

## Slide 20: Questions/Disscussion?