ITEM SPECIAL–SETTLEMENT PLATFORMS

Description: This item consists of furnishing, constructing, and maintaining settlement platforms and obtaining settlement readings as required by the plans or as directed by the Engineer.  At the option and expense of the Contractor, additional settlement platforms may be installed at locations approved by the Engineer.  Settlement readings shall be taken weekly during construction and during any specified waiting period.  The readings shall be plotted on graph paper presenting deformation (on the negative y-axis) and fill height (on the positive y-axis) versus time (on the x-axis). In order to create the graph, use the settlement platform spreadsheet located at http://www.dot.state.oh.us/divisions/engineering/geotechnical/geotechnical_documents/Blank_Settlement_Reading_Plots-English.xls in the OGE website Publications and Documents section. A copy of each cumulative plot shall be sent to the Office of Geotechnical Engineering, Attention: Geotechnical Design Coordinator, after each settlement reading is recorded.

Materials: Sound lumber such as 19mm (3/4-inch) exterior grade plywood shall be used for the base.  The pipe shall be 64mm (2-1/2-inch) standard black pipe with threaded fittings as shown on the plans.  A steel plate 915mm x 915mm x 3.2mm (36" x 36" x 1/8") may be substituted for the lumber for the platforms, at the Contractor’s option.

Construction Methods: The platform shall conform to the details shown on the plans.  The platform shall be set on a level surface.  The pipe shall be firmly secured to the platform and shall be maintained in a plumb position during the placement of the embankment.  The pipe shall be marked at intervals to facilitate measurement of the depth of fill.  The Contractor shall stop work in any location where the settlement platform has been disturbed or damaged.  Platforms or pipes damaged or displaced during construction shall be restored to their proper condition at the Contractor’s expense.

Prior to paving, the top of the settlement platform pipe shall be cut off 600mm (two feet) below the finished surface of the subgrade or finished ground surface, whichever is applicable.

Method of Measurement: The number of settlement platforms to be paid for shall be the actual number of settlement platforms completed, maintained, and accepted by the Engineer.

Basis of Payment: Payment shall be made at the contract unit price each for “Item Special – Settlement Platforms” which is compensation for constructing maintaining, and monitoring the settlement platforms including furnishing all labor, equipment, materials, and incidentals necessary to complete the work.  Payment shall not be made for settlement platforms which become useless due to damage caused by the Contractor’s operations.

(Note: A plan detail must accompany this note.)

Rev. 10-21-08