## Slide 1: ODOT QUICK DESIGN CLASS – VEGETATED BIOFTILER BMPS

## Slide 2: Overview
Vegetated Biofilter Design
Treatment Credit Considerations
Plan Components for Improved Construction
Performance Metrics / Maintenance

## Slide 3: Vegetated Biofiler
L&D Vol. 2 Section 1117.2.2
Provides quality treatment only (not quantity)

## Slide 4: Vegetated Biofilter Treatment Processes

## Slide 5: Design Process
Treatment Goals
Siting Analysis
Vegetated Biofilter Sizing

## Slide 6: Design Process
Treatment Goals
Siting Analysis
Vegetated Biofilter Sizing

## Slide 7: Project Example
Rural highway redevelopment
Improve shoulders
All within existing right-of-way

## Slide 8: Treatment % Calculations
Redevelopment: 20%
New Construction: 100%
All area within existing R/W is considered impervious for post-construction BMP calculations.
  But not for new R/W…

## Slide 9: Treatment % Calculations
Weighted treatment calculation:
  T% = Treatment %
  Aix = Project EDA that is inside the existing right-of-way (acres)
  Ain = Inside new permanent right-of-way, Ain is the new impervious area minus any impervious area that is removed (acres)

## Slide 10: Project Example – Treatment Goals
Project EDA = 3.0 ac
All within existing right-of-way
Aix = 3.0 ac; Ain = 0.0 ac
T% = [(Aix x 20)+(Ain x 100)] / (Aix + Ain)
T% = [(3.0 x 20)+(0.0 x 100)] / (3.0 + 0)
T% = 20%
20% x 3.0 ac = 0.6 ac

## Slide 11: Project Example – Treatment Goals
Project EDA = 3.0 ac >= 1 ac
  Need a post-construction BMP
Treatment % = 20%
  Required to treat 0.6 ac
All in existing right-of-way
  All existing right-of-way considered impervious
  Also, there is no new permanent right-of-way
  Therefore no “new impervious area in new permanent right-of-way”
  Water quality treatment only required

## Slide 12: ODOT Design Resources
ODOT Internet Site
Office of Hydraulic Engineering
Post Construction Storm Water BMP
BMP_Calcs_(Updated Jan 2017).xls
https://www.dot.state.oh.us/Divisions/Engineering/Hydraulics/Pages/PostConstructionStormWaterBMP.aspx

## Slide 14: ODOT Design Resources
BMP_Calcs_(Updated Jan 2017).xls

## Slide 15: ODOT Design Resources

## Slide 16: Design Process
Treatment Goals
Siting Analysis
Vegetated Biofilter Sizing

## Slide 17: Siting Analysis
Vegetated biofilters are at least 4 ft wide
Vegetated biofilters should receive unconcentrated flow along foreslope
Look for existing grass ditches to make a little wider
Use only if vegetated filter strip does not fit

## Slide 18: Siting Analysis

## Slide 19: Sheet Flow
0.16 acres
sheet flow

## Slide 20: Sheet Flow
L&D Vol. 2 Section 1116.1
  “For projects where the drainage sheet flows off the roadway and continues outside existing or proposed right-of-way, do not channelize flow for the sole purpose of providing a post-construction BMP. Treatment is not required for areas where sheet flow off the roadway continues to sheet flow outside ODOT right-of-way. Areas where this occurs should be documented in the post-construction BMP calculations and identified on the Project Site Plan.”

## Slide 21: Treatment Goals - Updated
Treatment not required for 0.16 ac sheet flow
(Project EDA – sheet flow) * T%
(3.0 ac – 0.16ac) * 20% = 0.57 ac
WARNING! Not This Way
(3.0 ac * 20%) – 0.16 ac = 0.44 ac

## Slide 22: Design Process
Treatment Goals
Siting Analysis
Vegetated Biofilter Sizing

## Slide 23: Siting Analysis

## Slide 24: Design Process
Treatment Goals
Siting Analysis
Vegetated Biofilter Sizing

## Slide 25: Vegetated Biofilter Sizing
Size a vegetated biofilter for each ditch and pick the best one for the project.

## Slide 26
Tributary Area
Notes: Reminder: Draw drainage basin boundaries perpendicular to contours
Look for drainage divides and for ditches

## Slide 27
Treatment Credit
Trib. Area = 4.0 ac
R/W Area = 1.1 ac

## Slide 28
Coefficient of Runoff – WQF BMP
Right-of-Way = 1.1 ac; C = 0.9
Woods = 2.9 ac; C = 0.3
Weighted C = [(1.1*0.9)+(2.9*0.3)] / (1.1+2.9) = 0.465

## Slide 29: Vegetated Biofilter Sizing
1
2
3

## Slide 30: Vegetated Biofilter Sizing
Area 1 (4.0 ac):
  1.1 ac within R/W; C=0.9
  2.9 ac woods; C=0.3
  (1.1ac * 0.9 + 2.9ac * 0.3) / 4.0 ac
  Weighted C = 0.465
  WQF = 0.465 * 0.65in/hr * 4.0ac = 1.209 cfs
  Treatment credit = 1.1 ac
  1.1 ac > 0.57 ac

## Slide 31: ODOT Design Resources
BMP_Calcs_(Updated Jan 2017).xls

## Slide 32: ODOT Design Resources

## Slide 33: Vegetated Biofilter Sizing
1
2
3

## Slide 34: Vegetated Biofilter Sizing
Area 2 (2.1 ac):
  1.3 ac within R/W; C=0.9
  0.8 ac woods; C=0.3
  (1.3ac * 0.9 + 0.8ac * 0.3) / 2.1 ac
  Weighted C = 0.67
  WQF = 0.67 * 0.65in/hr * 2.1ac = 0.915 cfs
  Treatment credit = 1.3 ac
  1.3 ac > 0.57 ac

## Slide 35: Vegetated Biofilter Sizing
1
2
3

## Slide 36: Vegetated Biofilter Sizing
Area 3 (0.6 ac):
  0.2 ac within R/W
  Since 0.2 ac < 0.57 ac treatment requirement, don’t go any further

## Slide 37: Vegetated Biofilter Sizing
Determine vegetated biofilter bottom width for Area 1 and Area 2: Manning’s Equation:
(0.15 for Vegetated Biofilter)

## Slide 38: Vegetated Biofilter Sizing
Q = WQF calculated using Rational Method
n = 0.15 (for flow within height of grass)
Depth <= 4 inches
Velocity <= 1 fps
Project Specific
Specified in L&D

## Slide 39: Vegetated Biofilter Sizing
Use a program or spreadsheet, given:
  Q
  n
  Channel geometry
  Longitudinal slope
Calculate
  Normal depth
  Average velocity

## Slide 40: Vegetated Biofilter Sizing
1

## Slide 41: Vegetated Biofilter Sizing – Area 1
Longitudinal slope = 0.01 ft/ft
Assume fore slope = 2:1
Assume back slope = 2:1
Manning’s n = 0.15
Q = 1.209 cfs
Use trial and error until you find a bottom width that gives a velocity <= 1 fps and a depth <= 4 in

## Slide 42: Vegetated Biofilter Sizing – Area 1
See FHWA Hydraulic Toolbox 4.20
See ODOT Excel spreadsheet

## Slide 43: ODOT Design Resources
BMP_Calcs_(Updated Jan 2019).xls

## Slide 44: ODOT Design Resources

## Slide 45: ODOT Design Resources

## Slide 46: Vegetated Biofilter Sizing
Area | Q | s | FS | BS | n | B | Vel. | Depth
 | cfs | ft/ft | H:V | H:V |  | ft | fps | in
1 | 1.209 | 0.01 | 2:1 | 2:1 | 0.15 | 8 | 0.44 | 3.83
2 | 0.915 | 0.01 | 2:1 | 2:1 | 0.15 | 6 | 0.43 | 3.84

## Slide 47: Vegetated Biofilter Sizing
1
2
3
8 FT
6 FT

## Slide 48: Vegetated Biofilter Sizing
Area 2 treatment credit = 1.3 ac
Only need 0.57 ac
Sub-delineate to reduce BMP size
2
6 FT

## Slide 49: Vegetated Biofilter Sizing – Area 2

## Slide 50: Vegetated Biofilter Sizing – Area 2
New area = 0.97 ac
  0.57 ac within R/W; C=0.9
  0.40 ac woods; C=0.3
  (0.57 ac * 0.9 + 0.40 ac * 0.3) / 0.97 ac
  Weighted C = 0.653
  WQF = 0.653 * 0.65in/hr * 0.97ac = 0.412 cfs
  Treatment credit = 0.57 ac
  0.57 ac = 0.57 ac

## Slide 51: Vegetated Biofilter Sizing
Area | Q | s | FS | BS | n | B | Vel. | Depth
 | cfs | ft/ft | H:V | H:V |  | ft | fps | in
1 | 1.209 | 0.01 | 2:1 | 2:1 | 0.15 | 8 | 0.44 | 3.83
2 | 0.915 | 0.01 | 2:1 | 2:1 | 0.15 | 6 | 0.43 | 3.84
2a | 0.412 | 0.01 | 2:1 | 2:1 | 0.15 | 3 | 0.39 | 3.54
2a | 0.412 | 0.01 | 2:1 | 2:1 | 0.15 | 4 | 0.36 | 3.02

## Slide 52: Vegetated Biofilter Sizing – Area 2

## Slide 53: Overview
Vegetated Biofilter Design
Treatment Credit Considerations
Plan Components for Improved Construction
Performance Metrics / Maintenance

## Slide 54: Vegetated Biofilter Treatment Credit
ODOT L&D Vol 2, Section 1117.2.2
Treatment Credit for Vegetated Biofilter is given to:
Areas within the project limits that sheet flow off of the roadway into a grassed shoulder, grassed foreslope, and then into a grassed trapezoidal ditch sized as described above. (Tributary areas to a Vegetated Biofilter that do not meet this criteria, i.e. drainage from concentrated flow or outside project limits, must be included in the determination of the EBW, but do not receive treatment credit.)
The area of the defined Vegetated Biofilter (the shoulder, foreslope, ditch bottom, and backslope) within the permanent right-of-way.

## Slide 55: Vegetated Biofilter Credit Example
Drainage Area

## Slide 56: Vegetated Biofilter Credit Example
Drainage Area
Enhanced Bankfull Width
Treatment Credit

## Slide 57: Vegetated Biofilter Credit Example
Drainage Area #1
Drainage Area #2

## Slide 58: Vegetated Biofilter Credit Example
Treatment Credit
Drainage Area #1
Drainage Area #2
Enhanced Bankfull Width
Treatment Credit

## Slide 59: Vegetated Biofilter Credit Example
Drainage Area #1
Drainage Area #2
Enhanced Bankfull Width
No Treatment Credit
Treatment Credit
(Width Still Sized for Both Drainage Areas)

## Slide 60: Vegetated Biofilter Credit Example
Drainage Area #1
Drainage Area #2
Offsite Drainage Area #3

## Slide 61: Vegetated Biofilter Credit Example
Drainage Area #1
Drainage Area #2
Enhanced Bankfull Width
No Treatment Credit
Treatment Credit
Offsite Drainage Area #3
(No Treatment Credit)
(Width Sized for All Drainage Areas)

## Slide 62: Overview
Vegetated Biofilter Design
Treatment Credit Considerations
Plan Components for Improved Construction
Performance Metrics / Maintenance

## Slide 63: Vegetated Biofilter Plan Components
Add 4” of Item 659 topsoil to the vegetated portion of the shoulder and foreslope
Add Item 670, Ditch Erosion Protection
Show vegetated biofilters on Project Site Plan
Call out vegetated biofilters on plan / profile sheets
Call out vegetated biofilters on cross sections

## Slide 64: Overview
Vegetated Biofilter Design
Treatment Credit Considerations
Plan Components for Improved Construction
Performance Metrics / Maintenance

## Slide 65: Performance Metrics
80% Grass Coverage on Foreslope, Bottom, and Backslope
No Ruts, Rills, Gullies, or Concentrated Flow
Flat Ditch Bottom
Remove Accumulated Trash and Sediment

## Slide 66: Initial Grass Establishment 80% Grass Coverage

## Slide 67: Initial Grass Establishment Rills & 80% Grass Coverage

## Slide 68: Don’t Mow When Wet Ruts & 80% Grass

## Slide 69: Erosion Protection and Catch Downcutting Early Gullies / Concentrated Flow

## Slide 70: Maintain Positive Drainage Don’t Design too Flat; Clear Downstream

## Slide 71: Maintenance
Keep Grass Alive
Mow at least Twice a Year
Don’t Mow when Wet
Catch Downcutting Early
After Sediment does Accumulate, must Regrade and Re-establish Grass
  Grading Different than Normal Ditching to Get Flat Bottom

## Slide 72: Questions ?
Jon Prier, P.E.
jonathan.prier@dot.ohio.gov
614-644-1876