RE 73-09

Rev. 9-2006

STATE OF OHIO

OHIO DEPARTMENT OF TRANSPORTATION

GUIDELINES FOR PREPARATION OF BUILDING REMOVAL PLANS

September, 2006

Overview:

Building Removal Plans should be prepared on all building removal contracts.  The plan shall basically consist of a modified right of way plan with the addition of a general summary.  The intent of these plans is to provide potential bidders and department personnel with a precise tool upon which to base their bids and to effect the removal of buildings acquired for highway improvements.  A detailed description of the required pages and information follows:

Title Page:

The Construction Title Page shall be used and adapted as follows:

- The statement “THIS PLAN FOR THE REMOVAL OF CERTAIN BUILDINGS ONLY (NOT CONSTRUCTION).  BUILDINGS IN THIS CONTRACT SHALL BE DEMOLISHED IN THEIR ENTIRETY AND DEBRIS/MATERIALS DISPOSED OF OFF-SITE, AS DIRECTED BY THE PROJECT ENGINEER.”  (APPLY TO THE TITLE SHEET AND GENERAL SUMMARY SHEETS).

- The OUPS (Ohio Utilities Protection Service) stamp shall be used.  OPUS can be reached at 1-800-362-2764

- The preparing agency, district, section, etc., shall be included and the R/W plan preparing consultant, etc., shall be removed.

- The correct year (most recent) specifications statement shall be used.  Under this shall appear the statement “I hereby approve these plans for removal of the buildings herein.”

- The signature of the Director of Department of Transportation is required on the title sheet.  The signature of the District Deputy Director can appear as well.

General Summary:

This page shall be an ODOT General Summary which includes the following columns, in this order:

- Sheet numbers, under which appears the word “lump” opposite the corresponding row for the particular reference number.

- The work “ITEM” under which appears the CMS reference “202.”

- The WORDS “GRAND TOTAL” under which appears the word “lump” opposite the specific reference number.

- The word or words “PARCEL” OR “PARCEL NUMBERS” under which appears the correct parcel numbers including all relevant suffixes (i.e, WL, WD, SL, T, etc.).

- A rather wide column with the word “DESCRIPTION” under which will appear the description of the items to be removed along with the property address.

- The words “REFERENCE NO.” under which appears the reference number corresponding to the same item on the detail sheet.

The statement “THIS PLAN FOR THE REMOVAL OF CERTAIN BUILDINGS ONLY, (NOT CONSTRUCTION), BUILDINGS IN THIS CONTRACT SHALL BE DEMOLISHED IN THEIR ENTIRETY AND DEBRIS/MATERIALS DISPOSED OF OFF-SITE, AS DIRECTED BY THE PROJECT ENGINEER.”

All affected utilities shall be listed with respective addresses and telephone numbers.

A legend showing the method used to define the buildings that are to be removed will appear on this page.

When appropriate the following note should be placed on pages 1 and 2.

NOTE:		CURRENTLY BUILDINGS ON THIS PROJECT ARE BEING INSPECTED FOR THE PRESENCE OF ASBESTOS.  THE CONTRACTOR SHALL NOT BE RESPONSIBLE FOR ASBESTOS ABATEMENT.

Detail Sheets:

The page or pages shall be copies of the R/W details sheets showing the affected parcels with structures to be removed, cross hatched and marked consistent with the legend on the general Summary Sheet.  Match lines shall be changed to reflect the new page numbers on the Building Removal Plan, as opposed to the right of way plan.  Reference numbers shall be delineated so as to be very clear after reduction and reproduction.  The buildings and appurtenances to be removed shall be cross hatched and the specific reference number shall point to all improvements.  Lastly, all pages shall be renumbered in order.