Designer Note:  Use the appropriate plan note below (based on highway type) on projects that use any funds from the American Recovery and Reinvestment Act.  The notes as written allow the contractor to determine appropriate locations for the signs with approval by the engineer.  Alternatively, specific locations can be indicated in the plans.  When specific locations are indicated, delete the first sentence in the second paragraph of the appropriate note(s).

Item 614 Modified American Recovery and Reinvestment Act (ARRA) Sign, Freeway/Expressway

This item shall consist of the furnishing and installing, and subsequent removal, of Modified American Recovery and Reinvestment Act (ARRA) signs on yielding post supports.

Install one ARRA sign near the beginning of the project in each route direction in a location as approved by the engineer.  The ARRA sign consists of one 120” x 84” white on green extrusheet sign with pictographs, one 120” x 24” black on orange extrusheet sign, and one 24” x 24” diamond flat sheet sign.  The sign fabrication details are found at:

http://www.dot.state.oh.us/Divisions/HighwayOps/Traffic/Pages/OTEHomePage.aspx

Install the sign on three No. 3 yielding posts as per Standard Drawing TC-41.20, with one post on sign centerline and one post 12” from each end.  Signs in protected locations may be installed on other supports as approved by the engineer.  Used signs are allowed provided they are in a condition acceptable to the engineer.  Remove the ARRA signs and supports at the end of the project.  Removed ARRA signs and supports are the property of the contractor.

Payment shall be included in the contract lump sum bid price for Item 614 Maintaining Traffic and shall include all labor, equipment, materials (including supports), tools and other incidentals to provide for a complete and accepted item of work.

Item 614 Modified American Recovery and Reinvestment Act (ARRA) Sign, Conventional Road

This item shall consist of the furnishing and installing, and subsequent removal, of Modified American Recovery and Reinvestment Act (ARRA) signs on yielding post supports.

Install one ARRA sign near the beginning of the project in each route direction in a location as approved by the engineer.  The ARRA sign consists of one 84” x 60” white on green extrusheet sign with pictographs, one 84” x 18” black on orange extrusheet sign, and one 18” x 18” diamond flat sheet sign.  The sign fabrication details are found at:

http://www.dot.state.oh.us/Divisions/HighwayOps/Traffic/Pages/OTEHomePage.aspx

Install the sign on two No. 3 yielding posts as per Standard Drawing TC-41.20, with one post 12” from each end.  Signs in protected locations may be installed on other supports as approved by the engineer.  Used signs are allowed provided they are in a condition acceptable to the engineer.  Remove the ARRA signs and supports at the end of the project.  Removed ARRA signs and supports are the property of the contractor.

Payment shall be included in the contract lump sum bid price for Item 614 Maintaining Traffic and shall include all labor, equipment, materials (including supports), tools and other incidentals to provide for a complete and accepted item of work.