## Slide 1: Evaluation of Viking-Cives® TowPlow for Winter Maintenance
William H. Schneider, IV
Christopher M. Miller
Mallory Crow
William A. Holik
State Job Number: 134704

## Slide 2: Acknowledgements
The University of Akron would like to thank the Division of Planning, Statewide Planning & Research Team:
Ms. Jill Martindale,
Ms. Kelly Nye,
Ms. Cynthia Gerst,
Ms. Vicky Fout, and
Mr. Scott Phinney.
And the Technical Liaisons:
Mr. Paul Ensinger,
Mr. Brian Olson, and
Mr. Mark Griffiths.

## Slide 3: Introduction
Snow and ice management is the single largest expenditure in the maintenance budget for the Ohio Department of Transportation (ODOT).
Goal to minimize costs while maximizing efficiency.
TowPlow is one piece of equipment being considered,
  Trailer with 27-foot blade and hopper / brine tank, and
  Rotates out to plow and treat a second traveling lane.
ODOT – Ashtabula County conducted pilot evaluation.
ODOT gain knowledge on new technologies.

## Slide 4: Project Setting

## Slide 5: Standard Truck
Single axle or tandem axle,
11 or 12 foot front plow usually sometimes 14 foot, and
Some may have additional wing plow – adding extra 5.5 feet of plowing.

## Slide 6: Standard Truck Comparison in Portage Co.
Truck opposite of TowPlow in Portage is tandem axle, 14 foot plow, with wing plow.
Treated opposite side of IR-76 while TowPlow treated other side.

## Slide 7: TowPlow System
Tandem axle truck with at least 350-horsepower engine.
TowPlow units equipped with hopper and brine tank.
Combined with front plow may clear 25 foot path.
Operate safely at 30 to 40 mph.
Image from Viking-Cives, www.vikingcives.com

## Slide 8: Data Collection

## Slide 9: Weather – NOAA Data
National Oceanic and Atmospheric Administration
Hourly snowfall data from NOAA’s National Operational Hydrologic Remote Sensing Centers
  One near each garage with a TowPlow.
Review total accumulating snowfall and peak hourly snowfall during an event to categorize:
  No Snowfall
  Trace Snowfall
  Light Snowfall
  Moderate Snowfall
  Heavy Snowfall

## Slide 10: Weather Data
Event Type | Number of Events
No Snow | 5
Trace | 8
Light | 27
Moderate | 15
Heavy | 5
Number of Events: 60
All Three Counties Events:

## Slide 11: Vehicle Delay
Delay created by TowPlow in various configurations is compared to delay created by Standard truck.
Bluetooth Technology is used to capture vehicle speeds.
Bluetooth Nodes placed along IR-76 in Portage County
Bluetooth nodes consist of:
  Bluetooth radio
  Computer board with USB interfaces
  Bluetooth Antennae
  3G wireless card
  Power regulator
  Batteries
Maintained weekly

## Slide 12
Eastern Route
Western Route

## Slide 13: Delay Analysis
Comparing expected travel time to actual travel time.
Delay based on three different storm categories determined using previous 4-hour snowfall
  Light: snowfall < 0.5 in
  Moderate: 0.5 in ≤ snowfall < 1 in
  Heavy: Snowfall ≥ 1 in
Analyzed three scenarios
Expected travel time based on baseline data
  Western Side – 65 mph
  Eastern Side – 66 mph

## Slide 14: Delay – TowPlow Treating Two Lanes and Standard Treating One Lane in Light Snow

## Slide 15: Delay – TowPlow Treating Two Lanes and Standard Treating One Lane in Heavy Snow

## Slide 16: Delay – Trucks Exit Highway in Heavy Snow

## Slide 17: Standard Truck Data

## Slide 18: TowPlow Data
Guidance Laser
DVR
Driver Camera
Passenger Side Camera
Rear Camera
Front Camera

## Slide 19: Video Documentation

## Slide 20: Video Documentation
2000 Hours of Video Used to Document:
  TowPlow Deployment
  TowPlow Treatment Change
  Front Plow Deployment
  New Route
  Lane Position Change

## Slide 21: TowPlow Deployment Definitions

## Slide 22: TowPlow Position Definitions

## Slide 23: Overall TowPlow Deployment
Event Type | Average (%)
Deployed Mileage | 53
Deployed Time | 56
Not Deployed Mileage | 47
Not Deployed Time | 44
Number of Events: 60
Overall TowPlow Status:
Percentage Over Evaluation
Deployment Status

## Slide 24: Overall Treatment Type
Event Type | Average (%)
Plowing Mileage | 91
Plowing Time | 91
Salting Mileage | 9
Salting Time | 9
Number of Events: 60
Overall TowPlow Treatment
Percentage Over Evaluation
Treatment Type

## Slide 25: Overall TowPlow Position
Event Type | Shoulder (%) | Right Lane (%) | Ramp (%)
Plowing Mileage | 23 | 69 | 8
Plowing Time | 23 | 66 | 12
Salting Mileage | 52 | 36 | 12
Salting Time | 53 | 33 | 14
Number of Events: 60
Overall Average TowPlow Lane Configuration:
Percentage Over Evaluation
Lane Position

## Slide 26: Cost
Annualized cost of TowPlow versus standard truck
Monte Carlo simulation
  Matlab
  Random number generator
Utilization rate for each truck by storm classification
TowPlow to standard truck equivalency
Comparison

## Slide 27: Variables

## Slide 28: Cost Variables
Sources:
ODOT – Specific operational and financial data.
M&R 661 – Forms filled out by operators with treatment, time, and location data.
NOAA – Weather data from stations near garages with TowPlows.
GPS/AVL & Video – Data collected from trucks.

## Slide 29: Utilization Rate (UR)
Need to determine how much the equipment is used to maintain the roadways during a winter event.
Determine an overall and by storm classification UR.

## Slide 30: Utilization Rate - Results
 | TowPlow | Standard
Overall | 54% | 65%
Trace | 17% | 18%
Light | 45% | 67%
Moderate | 72% | 96%
Heavy | 91% | 100%
TowPlow UR determined from video data collected.
Standard UR determined from GPS/AVL data and verification from M&R 661.
UR calculated for hours during event – not clean up time after

## Slide 31: Truck Equivalency
Not a 1:2 ratio – since TowPlow is not always able to be deployed or needed.
is the equivalent number of standard trucks needed to treat the same amount as the TowPlow.

## Slide 32: Truck Equivalency
Assume efficiencies are equal between both trucks.
Capacity of each truck is lane(s) treated in one pass:
  TowPlow Capacity is 2 lanes
  Standard Capacity is 1 lanes

## Slide 33: Truck Equivalency – Solving for Theta
Monte Carlo simulation – 1,000,000 times randomly select from range of UR to determine a distribution.
θ is determined to have an average of 1.706
Frequency – Number of Time Theta is Calculated in Simulation
Value of Theta (unit less)

## Slide 34: Annualized Cost
Monte Carlo simulation – 500,000 times
Average cost - $83,629 per year

## Slide 35: Cost Results
TowPlow has an annual savings averaging $22,551 per year.
1.4 standard trucks is break even point – no savings
More data presented in Chapter 6 of the Final Report

## Slide 36
Implementation

## Slide 37
Implementation – Potential Savings
 | 0 to 25 Events per Season | 26 to 50 Events per Season | 51 to 75 Events per Season | 76 to 100 Events per Season | 
Primarily Trace and Light Events (Some Moderate, No Heavy) | $4,100 to $12,000 | $13,100 to $17,400 | $17,900 to $20,800 | $20,800 to $24,100 | 
Primarily Light and Moderate (Some Trace, Some Heavy) | $4,100 to $12,800 | $13,800 to $17,500 | $18,500 to $21,400 | $21,200 to $25,800 | 
Primarily Moderate and Heavy (Some Light, Some Trace) | $4,100 to $12,900 | $14,300 to $17,500 | $20,000 to $29,000 | $22,500 to $29,200 | 
Note: The primary assumption of this table is that routes currently require two or more Standard trucks to maintain the expected LOS on the routes. One TowPlow compared to Equivalent (1.71) Standard ODOT Trucks. Used same simulation as Chapter 6, only modifying number of events in each weather classification. Weather classification is listed in Section 3.1 of this report. Standard deviation of events is set as 1, unless 0 events, then set to 0. Rounded to nearest hundreds place. Simulation repeated 100,000 times, five random weather distributions for each category presented above. |  |  |  |  | 
TowPlow Quantity | Standard Truck Quantity | TowPlow Cost | Standard Cost | Cost Difference
1 | 1.71 | $38,700 | $42,800 | $4,100
2 | 3 | $77,200 | $75,000 | ($2,200)
7 | 12 | $269,600 | $300,200 | $30,600
Note: The primary assumption of this table is that routes currently require two or more Standard trucks to maintain the expected LOS on the routes. No maintenance cost is included, and all events are set to zero, therefore the capital cost is the only factor. The discount rate is varied as in Chapter 6. Life of the truck pulling the TowPlow and Standard is eight years, while the TowPlow itself is expected to be 16 years. RED indicates higher annual cost for the TowPlow than the Standard truck. GREEN indicates lower annual cost for TowPlow than Standard truck. |  |  |  | 

## Slide 38: Thank You!